## Slide 1: IIR Filter

## Slide 2: MATLAB also has great resources for IIR filters
https://www.mathworks.com/help/signal/ug/iir-filter-design.html
IIR filter stands for infinite impulse response filter. h[n] of IIR filter has infinite length

## Slide 3: Advantages of IIR filters over FIR filters
IIR filters can achieve the same level of performance as FIR filters with less order
  How can IIR filter have less order than FIR filter when h[n] is of infinite

## Slide 4: Disadvantages of IIR filters over FIR filters
IIR filter have infinite length h[n]. Therefore, designers have to worry if the filter is stable, that is
Causal IIR filters can not have linear phase, but this may not matter in some applications

## Slide 5: IIR Filter Design Steps

## Slide 6: IIR Filter Design Steps
We only design low pass filters. Other type of filters are obtained by frequency shifting after a low pass filter design
Notes: Compare to FIR filter in Lec 20

## Slide 7: Prototype Analog Filters
To design the continuous-time filter, you also need the specifications, passband and stopband frequency and the relative/absolute ripples

## Slide 8: Converting between the specifications

## Slide 9: Classical Continuous-Time Filters
There are three approximations that are widely used in practice
  Butterworth lowpass
  Chebyshev (I and II) lowpass
  Elliptic lowpass

## Slide 10: Classical Continuous-Time Filters

## Slide 11: Butterworth Filter
You need the ‘s’ flag. Otherwise, Matlab will design a discrete-time filter

## Slide 12: Butterworth filter design: How to determine N and omegac?

## Slide 13: Butterworth continuous-time lowpass filter example

## Slide 14: Butterworth continuous-time lowpass filter example
N = 19
Almost linear phase in
passband

## Slide 15: Chebyshev Lowpass filter
Chebyshev-I filter have equiripple response in the passband
Chebyshev-II filter have equiripple reponse in the stop band
Chebyshev filters provide lower order than Butterworth filters for the same specification

## Slide 16: Chebyshev-I Lowpass filter

## Slide 17: Chebyshev-I filter design: How to determine N and omegac?

## Slide 18: Chebyshev-I continuous-time lowpass filter example

## Slide 19: Chebyshev-I continuous-time lowpass filter example
Equiripple in the passband
Definitely not linear phase

## Slide 20: Chebyshev-II continuous-time lowpass filter example

## Slide 21: Chebyshev-II continuous-time lowpass filter example
Equiripple in the stopband

## Slide 22: Elliptic Lowpass Filters

## Slide 23: Elliptic continuous-time lowpass filter example

## Slide 24: Elliptic continuous-time lowpass filter example

## Slide 25: Comparison of prototype filters

## Slide 26: Still to do
1) Convert continuous-time filter to discrete-time filters
2) Frequency transform lowpass filter to bandpass, highpass, etc. depending on application

## Slide 27: Convert continuous-time filter to discrete-time filters
Many procedures for converting continuous-time filter to discrete-time filter
1) impulse-invariance transformation
2) bilinear transformation (most widely used)

## Slide 28: Convert continuous-time filter to discrete-time filters

## Slide 29: Impulse-Invariance Transformation

## Slide 30: Impulse-Invariance Transformation
Even if the continuous-time filter satisfies all the specifications, it may be the case that the discrete-time filter after impulse-invariance transformation does not satisfy the specifications
  Reason why impulse-invariance transformation is not widely used
Td = design sampling period, Fd = 1/Td = design sampling frequency
To convert between passband/stopband frequencies of continuous-time filter to digital filter
or

## Slide 31: Digital Chebyshev-I using impulse invariance

## Slide 32: Digital Chebyshev-I using impulse invariance

## Slide 33: Digital Chebyshev-II using impulse invariance

## Slide 34: Digital Chebyshev-II using impulse invariance
Does not satisfy design specification!

## Slide 35: Bilinear transformation is the better alternative
Bilinear transformation also uses the sampling period Td but it does not affect the transformation. So you can use any value

## Slide 36: Bilinear transformation

## Slide 37: Digital Chebyshev-II using bilinear transformation

## Slide 38: Digital Chebyshev-II using bilinear transformation

## Slide 39: Frequency transform lowpass filter to bandpass, highpass, etc. depending on application
Using designed lowpass digital filter we want to design other kinds of filters:
  Lowpass
  High-pass
  Band-pass
  Band-stop
This requires a frequency-domain transformation from one z-plane to another z-plane
Design CT
LP Filter
z → z
Frequency Band
Transformation
Apply
CT → DT
Transformation
Desired IIR
Filter

## Slide 40: Frequency transform lowpass filter to bandpass, highpass, etc. depending on application
1) Given desired (highpass, bandpass, bandstop) discrete-time filter specifications, we want to convert the frequency specifications to a lowpass filter specification (Design Parameters)
2) Design the discrete-time IIR lowpass filter
3) Map the system function of the lowpass filter to desired filter’s system function (Transformation)

## Slide 42: Finding the design parameters
Ldenote the frequency of the discrete-time lowpass filter
  = cut off frequency of discrete-time lowpass filter
  = passband frequency of discrete-time lowpass filter
  = passband frequency of discrete-time lowpass filter
Let denote the frequency of the desired (highpass, bandpass, bandstop) discrete-time filter
  = cut off frequency of desired filter
  = passband frequency of desired filter
  = stopband frequency of desired filter

## Slide 43: Highpass filter design example
Specifications
Stopband edge: radian
Passband edge: radian
Stopband attenuation: As = 15dB
Passband ripple: Ap = 1dB
We need to find lowpass filter equivalent and
But there is only 1 equation and 2 unknown. So, we arbitrarily set
Find using and

## Slide 44: Highpass filter design example
Once we have the system function, H(z), of the low pass filter using bilinear transformation
Whenever you see z-1 in H(z), replace with the transformed expression

## Slide 45: Filter types

## Slide 46
not the same thing!